## Slide 1: Hydra
Automated Plant Watering System

## Slide 2: What is Hydra?
Is a microcontroller-based automatic plant watering system.

## Slide 3: Hydra Modules
Hydra Root Module and the Hydra Leaf Module

## Slide 4: Hydra Root Module
The Hydra Root Module controls the overall management of the Hydra Network including all connected Hydra Leaf Nodes.

## Slide 5: Hydra Leaf Module
The Hydra Leaf Module controls the specific branch. It is responsible in checking the soil moisture and request to the Hydra Root for a water distribution.

## Slide 6: Features

## Slide 7: Hydra Features
Automated watering based on user preferences such as time-based watering or when the soil is dry.
Upgradable up to 16 independent on-field watering modules.
Automatically detect the water level in the tank and initiates a refill process.
Hydra Leaf is battery-powered that could run approximately 14 days to 31 days based on battery capacity.
Data logging feature.
Able to compute water consumption from different connected Hydra Leaf and adjusts automatically based on its consumption.
Sends a text message to the user of system activities based on user preferences.

## Slide 8: Water Distribution Setup
Water Distribution Setup is based on the pump configuration either discharge only, no pump attached, discharge-refill configuration or either of the three.

## Slide 9: Legend
Water Valve
Water Flow Sensor
Water Drip/ Atomizer
Hose/ Water Line
Water Flow Direction
Optional Water Line

## Slide 10: Discharge Only
Source
Tank
Pump
Drain
Field Lines
Branch Line
Distribution Line
Drain
Line
Source
Line
Tank-based
Stable Main Water Source Pressure
Pump is configured for water discharge purposes only
Drain is optional
Best suited for having a stable main water source water pressure esp. those with connections from the water district.

## Slide 11: Direct Distribution
Pump
Source
Field Lines
Branch Line
Distribution Line
Source
Line
Unstable Main Water Source Pressure
Pump is configured for water discharge purposes only
Applicable only to main water source such as well.

## Slide 12: Discharge-Refill
Source
Tank
Pump
Drain
Field Lines
Branch Line
Distribution Line
Drain
Line
Source
Line
Tank-based
Able to switch from direct source distribution, tank refill and tank-based water discharge.
Drain is optional.
Suitable for either stable and unstable water source pressure.
Discharge
Line
Discharge
Line

## Slide 13: Components

## Slide 14: Soil Moisture Sensor
Features:
Digital and analog output
Working voltage: 3.3V-5V On-board LM393 chip
Dimension: 3.2cm * 1.4cm
Price: Php. 55

## Slide 15: Plastic Water Solenoid Valve
Features:
½ inch diameter PVC pipe
12V powered
Minimum pressure requirement of 0.02 Mpa (3 PSI)
Price: Php. 250

## Slide 16: Plastic Water Flow Sensor
Features:
½ inch diameter PVC pipe
5V - 12V powered
13.1 (L/min) output readings
Price: Php. 247

## Slide 17: Ultrasonic Ranging Sensor
Features:
½ inch diameter PVC pipe
5VDC powered
Effective angle for computation: < 30 degrees
Ideal distance: 2cm to 500 cm
Ultrasonic Frequency: 40k Hz
Price: Php. 60

## Slide 18: Relay Module
Features:
Power output: 250V AC 10Amps/ 125V DC 10 AMps
5V DC low level trigger
16-channel relay variation
Price: Php. 155 (4-channel)

## Slide 19: MicroSD Card Reader Module
Features:
Supports Micro SD cards, Micro SDHC card (high speed card)
Price: Php. 79

## Slide 20: NodeMCU V3 ESP8266 ESP-12E
Features:
Communication interface voltage: 3.3V.
Antenna type: Built-in PCB antenna is available.
Wireless 802.11 b/g/n standard
WiFi at 2.4GHz, support WPA / WPA2 security mode
Power input: 3V
Range: ~250 meters
Price: Php 160